## Slide 1: Hydrogen Production in ERCOT
Chart: Industrial Level Wind Power
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
 | 33.6 | 33.6 | 33.6 | 172.92 | 173 | 925 | 1085 | 1286 | 1286 | 1755 | 2738 | 4490 | 7431 | 9384 | 9958 | 10367.4 | 12185 | 12328 | 14000.2 | 17664 | 20187.8

## Slide 2: Hydrogen from Electrolysis
Detailed financial analysis by NREL over a 40 year investment period
Feedstock costs are the main cost driver when producing hydrogen using electrolysis
  77 % of cost for centralized plant
  57 % of cost for decentralized plant
The feedstock cost is the cost of electricity and water to the electrolysis
  Electricity totally dominates
Chart: 
| Revenues $/kg H2 | Expenses $/kg H2 | Revenues $/kg H2 | Expenses $/kg H2
Cost of Hydrogen | 5.253 | 1.7474
Salvage Value | 0.023539 | 0.02567
Byproduct Sales | 0 | 0

Feedstock Cost | 3.9641 | 0
Fixed Operating Cost | 0.4789 | 0.46362
Initial Equity Depreciable Capital | 0.43887 | 0.47859
Other Variable Operating Costs | 0.015367 | 0.47386
Debt Interest | 0.23099 | 0.2519
Principal Payment | 0.096931 | 0.1057
Yearly Replacement Costs | 0.10347 | 0.064214
Decommissioning Costs | 0.023539 | 0.02567
Chart: 
| Revenues $/kg H2 | Expenses $/kg H2
Cost of Hydrogen | 5.1754
Salvage Value | 0.0036162
Byproduct Sales | 0

Feedstock Cost | 3.9953
Fixed Operating Cost | 0.46243
Initial Equity Depreciable Capital | 0.31372
Debt Interest | 0.18687
Yearly Replacement Costs | 0.14839
Taxes | 0.02556
Cash for Working Capital Reserve | 0.020325
Other Variable Operating Costs | 0.011305
Centralized PEM Electrolysis
Distributed PEM Electrolysis
Chart: Industrial Electricity

## Slide 3: Hydrogen from Natural Gas
NREL has calculated the cost of centralized production of hydrogen from natural gas with carbon capture.
Case study example of a plant producing hydrogen at 340 ton/day
The process produce 9.26 CO2 kg/kg H2, whereof 8.33 kg CO2/kg H2 is captured and 0.93 kg CO2/ kg H2 is emitted
  Amounts to a capture rate at 90 % of produced CO2
Chart: 
| Revenues $/kg H2 | Expenses $/kg H2
Cost of Hydrogen | 1.5582
Salvage Value | 0.0015603
Byproduct Sales | 0

Feedstock Cost | 0.82525
Other Variable Operating Costs | 0.20562
Initial Equity Depreciable Capital | 0.14358
Yearly Replacement Costs | 0.12137
Fixed Operating Cost | 0.11952
Debt Interest | 0.09432
Taxes | 0.027744
Cash for Working Capital Reserve | 0.015686
Capital Costs | 
H2A Total Direct Capital Cost | $202 246 784
H2A Carbon Sequestration Total Direct Capital Cost | $137 971 172
Indirect Depreciable Capital Costs | $142 891 542
Total Capital Costs | $484 210 222
Chart: Industrial Natural Gas

## Slide 4: ERCOT Load Zones
ERCOT is divided into 8 load zones where we have historical prices
Both prices from the Day-ahead (DAM) and Real-time (RTM) markets are available
The mean prices are the same but RTM is more fluctuating: STD(RTM) = 3xSTD(DAM) for 2017
Load zone | DAM - MEAN | DAM - STD | RTM - MEAN | RTM - STD
AEN | 24.69 | 10.15 | 24.84 | 33.59
CPS | 25.62 | 10.96 | 26.04 | 51.05
HOUSTON | 29.02 | 16.56 | 29.17 | 69.01
LCRA | 24.97 | 10.66 | 25.02 | 35.25
NORTH | 23.89 | 9.65 | 23.73 | 25.54
RAYBN | 23.66 | 9.02 | 23.52 | 24.83
SOUTH | 28.91 | 14.77 | 28.04 | 45.69
WEST | 23.72 | 10.60 | 23.57 | 29.35

## Slide 5: Hydrogen Production from Electrolysis
Current cost of producing hydrogen from electricity in ERCOT
Place a 50 ton per day electrolysis plant in respective load zones
Assume it does not affect the electricity price
What is the optimal configuration of a flexible plant?
  Results:
 | Day-ahead Market |  | Real-time Market | 
Load zone | Electrolyzer [MW] | Storage [Nm3] | Electrolyzer [MW] | Storage [Nm3]
AEN | 123.4176 | 69521.69 | 116.5914 | 121611.7
CPS | 124.1889 | 76473.86 | 117.3808 | 150126.5
HOUSTON | 133.7024 | 115869.5 | 119.3578 | 139043.4
LCRA | 123.6034 | 72034.52 | 116.7803 | 126378.6
NORTH | 120.3827 | 69521.69 | 116.9896 | 108144.9
RAYBN | 118.7894 | 69521.69 | 115.3533 | 101122.5
SOUTH | 131.9882 | 115869.5 | 121.7034 | 155596.2
WEST | 121.8031 | 86228.45 | 120.2367 | 141193.5
MEAN | 124.73 | 84380.11 | 118.05 | 130402.15

## Slide 6: Hydrogen Cost from Electrolysis - ERCOT
RTM – Real-time market
DAM – Day-ahead market
Flex – with storage
Const – without storage
As the mean electricity price is the same in both markets. procuring hydrogen at a constant level gives the same costs
When hydrogen is produced flexibly. the RTM market gives lower costs as it has periods with very low costs where we can produce hydrogen cheaper.
However. using perfect foresight for the RTM market is not realistic as the low prices arise from uncertainties in renewable energy production
  A flexible system can react to these uncertainties and take advantage of the low prices
  But storage strategies are too good when we have perfect foresight and would not be achievable in practice
PS: grid tariffs are not included here, network zones don’t directly overlap with load zones

## Slide 7: Nordpool
 | MEAN | STD
SYS | 29,40757 | 5,175868
SE1 | 30,84111 | 7,158612
SE2 | 30,84111 | 7,158612
SE3 | 31,23813 | 7,968093
SE4 | 32,18019 | 8,946456
FI | 33,19174 | 9,61076
DK1 | 30,08477 | 10,67856
DK2 | 31,96569 | 10,98284
Oslo | 29,03505 | 4,878746
Kr.sand | 28,83175 | 4,625652
Bergen | 28,83855 | 4,536337
Molde | 29,52928 | 5,540113
Tr.heim | 29,52928 | 5,540113
Tromsø | 25,72827 | 5,238795
EE | 33,20384 | 9,543607
LV | 34,67895 | 10,35208
LT | 35,13181 | 10,80792
AVG | 30,84 | 7,57
TEXAS | 23,72 | 10,60
Higher prices and lower price variation than Texas

## Slide 8: Hydrogen Cost from Electrolysis - Nordpool
Producing hydrogen in the regulating market is cheaper than from the spot market in Sweden, Finland and Denmark but not in Norway
Flexible production don’t have significantly impact on the costs of hydrogen production due to low price variations
Generally more expensive than Texas due to higher electricity prices, hydrogen production in Northern Norway (Tromsø) is the only one that is competitive with Texas

## Slide 9: Natural Gas Henry Hub
Chart: Industrial Natural Gas – NREL case